## Slide 1
🚇
AI/ML Fundamentals — Capstone Defense
Short-Term Metro Passenger
Flow Forecasting
Predicting station inflow 15 minutes ahead for proactive crowd management
Muhammad Murodov
Individual Project Track · Live demo: metro-flow-forecasting.streamlit.app
Notes: Opening (0:00-0:30): Metro operators manage safety from a control room, but today they only see crowding after it appears. This project gives them a 15-minute head start.

## Slide 2
The problem: crowding is seen too late
Who: metro control-room operators.
Today they rely on CCTV and staff observation, so a train, gate, or staff move only happens after a platform is already full.
At rush hour, trains arrive every 1.5–5 min — a platform fills faster than staff can react.
The ML task
Supervised time-series regression.
Input: station + recent flow history + calendar.
Output: predicted inflow for the next 15-min interval → crowding band.
What the forecast changes
✗
React
once the platform is full
↓
✓
Prepare
before it fills — 15 min of lead time
Advisory only — supports human dispatch, never automated control of trains or gates.
2
Notes: User + task (0:30-1:15): The user is control-room staff. The system converts 'react once full' into 'prepare before it fills'. ML task: supervised time-series regression predicting next-interval inflow. It is advisory, not automated control.

## Slide 3
Data & approach
HZMetro (Hangzhou Metro) · Zenodo DOI 10.5281/zenodo.3145404 · CC-BY 4.0
1
Raw AFC taps
80 stations · 25 days · ~1.3 GB
→
2
Aggregate
day-by-day → 15-min inflow/outflow
→
3
Features
calendar + lags 1–4 + rolling mean
→
4
Model
predict next-interval inflow
Leakage control is the backbone of the split
✓
Chronological split Train Jan 1–18 · Val 19–20 · Test 21–25. No shuffling — future never leaks into the past.
✓
Fit on train only Scalers/encoders fit on the training split; test statistics stay unseen.
✓
Past-only features Lags & rolling means computed within each station using strictly earlier intervals.
✓
Test touched once The held-out test set is scored a single time, after model selection on validation.
3
Notes: Data + approach (1:15-2:10): HZMetro, 80 stations, 25 days, CC-BY 4.0. Raw taps aggregated day-by-day to 15-min flow. The key discipline is leakage control: chronological split, scalers fit on train only, past-only lag features, test touched once.

## Slide 4
Results: XGBoost wins, and I can say why
Model | Target | Val MAE | Test MAE
Historical Average (baseline) | inflow | 29.34 | 37.55
Ridge regression | inflow | 29.29 | 39.29
XGBoost (selected) | inflow | 22.42 | 25.75
XGBoost | outflow | 21.23 | 23.79
~24%
lower MAE than the baseline (val)
25.75
test MAE (passengers)
3 runs
tracked in MLflow
!
Honest weakness — error is not uniform
Morning peak is hardest (MAE ~46) vs off-peak (~19). Normalised by volume the error rate is fairly steady (~11–16%).
Busy stations have higher absolute error; quiet stations have the highest relative error — which is why MAPE was reported with caution for low-count night intervals.
4
Notes: Result + weakness (2:10-3:10): XGBoost was selected on validation MAE (22.42), ~24% better than the Historical Average baseline; test MAE 25.75. Honest weakness: error is largest at the morning peak and quiet stations have the highest relative error, which is why MAPE was used cautiously.

## Slide 5
The demo: one input → one decision
INPUT
Station
+ current 15-min interval
→
MODEL
XGBoost
loads frozen artifact, no retraining
→
OUTPUT
Predicted inflow
+ crowding band
🟢 Low
passengers < 100
🟡 Medium
passengers 100–300
🔴 High
passengers > 300
Two ways to run it
Deployed app
inflow/outflow selector, trend chart, network crowding map
05_demo.ipynb
clean Colab run: station + time → forecast
Invalid or too-early intervals are rejected with a clear message instead of crashing.
5
Notes: Showcase + demo (3:10-4:20): Input a station and a current interval; the frozen XGBoost artifact predicts next-interval inflow and maps it to a crowding band. Two routes: the deployed Streamlit app and the clean 05_demo notebook. Invalid inputs are rejected safely.

## Slide 6
Responsible use & limitations
🔒
Aggregate 15-min counts only. No passenger identity, trips, or biometric data anywhere in the pipeline.
Privacy
⚖️
Single city (Hangzhou). Accuracy varies by station & time — quiet stations have the highest relative error.
Fairness
📅
25 days captures daily & weekly patterns but no seasonality, holidays, or weather.
Short window
🚇
Won't deploy to Tashkent as-is (different topology, culture, calendar). Motivation, not a claim.
No direct transfer
6
Notes: Responsible use: aggregate counts only (no personal data); single-city fairness caveat; 25-day window means no seasonality; and no direct transfer to Tashkent. State these as limitations, not weaknesses to hide.

## Slide 7
What I'd do next
1
LSTM sequence model — Compare representation-learning against the feature-engineered XGBoost (stretch goal).
2
Prediction intervals — Surface uncertainty, not just a point forecast — operators act on ranges.
3
Tashkent transfer — Retrain on local AFC data once available; the pipeline is the reusable asset, not the weights.
A simple project done correctly beats a complex one done poorly. Repo: github.com/muhammadmurodov/metro-flow-forecasting
7
Notes: Next improvement (4:20-5:00): LSTM as a stretch comparison, prediction intervals for uncertainty, and Tashkent transfer by retraining on local data. Close on: a simple project done correctly beats a complex one done poorly.